BLUETOOTH BASED INDUSTRIAL DATA ACQUISITION SYSTEM

DESCRIPTION

Bluetooth is a wireless module which transfers data from dongle to blue tooth modem and modem to Bluetooth dongle. This module enables you to transmit & receive wireless data in serial format. It is an advanced technology which can is widely used now-a-days in mobile data sharing and within network communications like modem to printer, etc… allowing transparent two way data communication. In our project we can simply use it for transmitting wireless serial data to establish connection between MCU or embedded project and PC.

In this project we are connecting  heart beat, temperature sensor to monitor patient condition.  Microcontroller reads data from sensors and sends to Bluetooth modem. Modem sends data to Dongle, Bluetooth modem is connected to microcontroller serially with 9600 baud rate.  The range of Bluetooth modem is 10 meters with frequency 2.4 GHz. Blue tooth Transmit power is 4dBm and sensitivity is 84 dBm. Here in our project Bluetooth modem acts as receiver and Bluetooth dongle acts as transmitter which is connected to USB port of the PC. Inside the PC we have an application(c# .net) which takes data from dongle and display on GUI. GUI is a software application which is very useful using which we can easily identify parameters and even we have a provision that the parameters status can be played back in audio format also as announcement from PC Speakers. Our project very near to the real time industry applications.

Here we use an 8051 microcontroller with 5V DC Power supply. Serial (UART) protocol is primary concern here. The heart of this project is Bluetooth modem which works on serial (UART) protocol. Microcontroller is interfaced with two digital sensors (Level, Smoke) and one Analog sensor (LM35). All sensors are positive triggered.

# TECHNICAL SPECIFICATIONS

HARDWARE

Micro controller	:	AT89S52

Crystal			:	11.0592 MHz

LED			:	5mm Red LED

Blue Tooth Modem

ADC			:	LM35

Smoke sensor		:	MQ200

Level sensor		:	Wire leads

Basic GPIOs

POWER SUPPLY

Transformer		:	12V step down

Filter			: 	1000uf/25V

Voltage Regulator	:	7805 / 7812

SOFTWARE

Software tools used

Keil IDE

Proteus VSM

UC flash

C# .net application

APPLICATIONS

- Industrials

- Sensor Networking

BLOCK DIAGRAM

POWER SUPPLY BLOCK DIAGRAM

# Text boxes

Bridge Rectifier

PC C# (.net) Application

Output

Regulator

Filter

Step down Transformer

Max-232

Blue Tooth Modem

Heart beat sensor

LM35

Power Supply

8

0

5

1

Level Sensor

ADC 0804

Blue Tooth Dongle