DAM GATE CONTROL SYSTEM

DESCRIPTION:

The project is aimed to design a “DAM GATE CONTROL SYSTEM” through which we can automate the dam gates, without human intervention.

The project is designed in such a way that the micro controller 8051 is interfaced to three water level sensors which are placed at 3 levels of water in the reservoir. The status of the sensors will be continuously monitored by the micro controller, if the sensor at level 3 is sensed in the water the corresponding signal will be passed to the controller and it will take the intelligent decision of rotating the motor which is interfaced to the controller and is connected to the gate, so that the gate will be opened. Likewise, for the levels 1 &2 the gate will be closed as per the code logic. Here a16x2 LCD is provided to display the status of the gate whether it is opened or closed.

This project uses regulated 5V, 500mA power supply. Unregulated 12V DC is used for geared motor. 7805 three terminal voltage regulator is used for voltage regulation. Full wave bridge rectifier is used to rectify the ac output of secondary of 230/12V step down transformer.

# TECHNICAL SPECIFICATIONS:

HARDWARE:

Micro controller	:	AT89x series

Crystal			:	11.0592 MHz

LCD			:	HD44780

Water level sensor

Driver IC		:	L293D

DC motor

Power supply

Transformer		:	12V step down

Filter			: 	1000uf/25V

Voltage Regulator	:	7805, 7812

SOFTWARE:

Keil IDE

UC flash

Proteus

APPLICATIONS:

Dam gates

Reservoirs

Irrigation control

BLOCK DIAGRAM:

POWER SUPPLY BLOCKDIAGRAM:

# Text boxes

DRIVER IC L293D

DC MOTOR

Power Supply

8

0

5

1

WATER

LEVEL

SENSOR1

WATER

LEVEL

SENSOR3

WATER

LEVEL

SENSOR2

16X2

LCD

Step down Transformer

Filter

Regulator

Output

Bridge Rectifier